## Processing For Packets Routed By The Firewall
Queue Type	Queue Function	Packet Transformation Chain in Queue	Chain Function
Filter	Packet filtering	FORWARD	Filters packets to servers accessible by another NIC on the firewall.
		INPUT	Filters packets destined to the firewall.
		OUTPUT	Filters packets originating from the firewall
Nat	Network Address Translation	PREROUTING	Address translation occurs before routing. Facilitates the transformation of the destination IP address to be compatible with the firewall's routing table. Used with NAT of the destination IP address, also known as destination NAT or DNAT.
		POSTROUTING	Address translation occurs after routing. This implies that there was no need to modify the destination IP address of the packet as in pre-routing. Used with NAT of the source IP address using either one-to-one or many-to-one NAT. This is known as source NAT, or SNAT.
		OUTPUT	Network address translation for packets generated by the firewall. (Rarely used in SOHO environments)
Mangle	TCP header modification	PREROUTING / POSTROUTING / OUTPUT / INPUT / FORWARD	Modification of the TCP packet quality of service bits before routing occurs. (Rarely used in SOHO environments)

## Descriptions Of The Most Commonly Used Targets
target	Desciption	Most Common Options
ACCEPT	iptables stops further processing. / The packet is handed over to the end application or the operating system for processing	N/A
DROP	iptables stops further processing. / The packet is blocked	N/A
LOG	The packet information is sent to the syslog daemon for logging / iptables continues processing with the next rule in the table / As you can't log and drop at the same time, it is common to have two similar rules in sequence. The first will log the packet, the second will drop it.	--log-prefix "string" / Tells iptables to prefix all log messages with a user defined string. Frequently used to tell why the logged packet was dropped
REJECT	Works like the DROP target, but will also return an error message to the host sending the packet that the packet was blocked	--reject-with qualifier / The qualifier tells what type of reject message is returned. Qualifiers include: / icmp-port-unreachable (default) / icmp-net-unreachable / icmp-host-unreachable / icmp-proto-unreachable / icmp-net-prohibited / icmp-host-prohibited / tcp-reset / echo-reply
DNAT	Used to do destination network address translation. ie. rewriting the destination IP address of the packet	--to-destination ipaddress / Tells iptables what the destination IP address should be
SNAT	Used to do source network address translation rewriting the source IP address of the packet / The source IP address is user defined	--to-source <address>[-<address>][:<port>-<port>] / Specifies the source IP address and ports to be used by SNAT.
MASQUERADE	Used to do Source Network Address Translation. / By default the source IP address is the same as that used by the firewall's interface	[--to-ports <port>[-<port>]] / Specifies the range of source ports to which the original source port can be mapped.

## General Iptables Match Criteria
iptables command Switch	Desciption
-t <-table->	If you don't specify a table, then the filter table is assumed. As discussed before, the possible built-in tables include: filter, nat, mangle
-j <target>	Jump to the specified target chain when the packet matches the current rule.
-A	Append rule to end of a chain
-F	Flush. Deletes all the rules in the selected table
-p <protocol-type>	Match protocol. Types include, icmp, tcp, udp, and all
-s <ip-address>	Match source IP address
-d <ip-address>	Match destination IP address
-i <interface-name>	Match "input" interface on which the packet enters.
-o <interface-name>	Match "output" interface on which the packet exits

iptables -A INPUT -s 0/0 -i eth0 -d 192.168.1.1 -p TCP -j ACCEPT

## Common TCP and UDP Match Criteria
Switch	Desciption
-p tcp --sport <port>	TCP source port. Can be a single value or a range in the format: start-port-number:end-port-number
-p tcp --dport <port>	TCP destination port. Can be a single value or a range in the format: starting-port:ending-port
-p tcp --syn	Used to identify a new TCP connection request. ! --syn means, not a new connection request
-p udp --sport <port>	UDP source port. Can be a single value or a range in the format: starting-port:ending-port
-p udp --dport <port>	UDP destination port. Can be a single value or a range in the format: starting-port:ending-port

iptables -A FORWARD -s 0/0 -i eth0 -d 192.168.1.58 -o eth1 -p TCP --sport 1024:65535 --dport 80 -j ACCEPT

iptables -A OUTPUT -p icmp --icmp-type echo-request -j ACCEPT

iptables -A INPUT -p icmp --icmp-type echo-reply -j ACCEPT

iptables -A INPUT -p icmp --icmp-type echo-request -m limit --limit 1/s -i eth0 -j ACCEPT
iptables -A INPUT -p tcp --syn -m limit --limit 5/s -i eth0 -j ACCEPT

iptables -t nat -A POSTROUTING -s 192.168.1.100 -o eth0 \
        -j SNAT --to-source 97.158.253.26
iptables -t nat -A PREROUTING -d 97.158.253.26 -i eth0 \
 -j DNAT --to-destination 192.168.1.10